SKELDO®

# Heat shrinkable cable accessories

## Shrinkable tubes

Shrinkable cable caps

Cable joints

Cable terminations

Repairing sleeves

etc.

# Tools , Crimping tools

SKELDO  s.r.o.                                Tel.+fax.    +420 - 377 246 372

Radynska  24 ,  326 00  Plzen            E-mail :  skeldo@skeldo.cz

Czech republic				                http://www.skeldo.cz

## 1. Heat shrinkable polyolefine tubes

both sealant lined and

without the inside wall

sealant

### General use

- cable ending sand sealing of electric terminal connector

- to connect groups of conductors

- for power and telecommunication cable joints

- to repair damaged insulation of cables

- to insulate sticks and other objects

- to repair or joint tubes (e.g. water pipes)

- for mechanic and anticorrosive protection of conductor and other materials

- coloured tubes as decorative elements

#### Shrinking

- shrinking temperature more than 120ºC by hot air or soft yellow flame

Specifications

- volume resistivity			min.			1013 Ω.cm

- dielectric strength			min.			15   kV/mm

- tensile strength			min.			12   MPa

- longitudial change			max.			15 %

- shrink temperature						120ºC – 200ºC

- shrink ratio				2 : 1        step to	3 : 1

- acceptable working temperature				-55ºC -  + 105ºC

- heat shock resistance /4 h./					200 ± 3ºC

- water absorption			max.			0,2 %

- density								0,93 g/cm

##### Basic distinction

- thin wall  RCACS, RCK , RCz , RCADW type

- medium wall RP , RPz , RPK , RPKz , RD , RDK type

- thick wall RG , RGK type

- RCACS , RCz , RP , RPz , RG , RD types without the inside wall sealant

- RCADW , RCK , RPK , RPKz , RGK, RDK – sealant lined

Storing:

In a sheltered place or warehouse from –10ºC to +35ºC

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

###### 1.1.1 Thin wall heat shrinkable

highly flame retardant

tubes -RCACS type

- flexible

- highly flame retardant

- environment friendly

- free from heavy metals and harmful substances such as PBB’s, PBBO’s, PBBE’s

- without the inside wall sealant

- good resistance against solvents and chemicals

- easy to cut

- colours: black – standart colour

it’s possible to arrange other colours according to the type and amount of the

particular artefact – red, green,blue, yellow, white and transparent

- lengths: basic 1m, after an agreement even others, for example 50m on a spool

- minimum shrink temperature 70ºC by hot air or soft yellow flame

- minimum full recovery temperature 100 ºC

- general use in industry as electric insulation from –55ºC up to +125ºC

Packing: in closed folio with type indication

Storage:  in a sheltered place, temperature from –10ºC  up to +35ºC

##### Dimensions and types

Inside diameter 		              Wall thickness

Nr.                    Type	              	        before and after	                   after complete shrinking

d1  mm  d2                                                            t mm

148101..	RCACS 1,6 / 0,8			1,6         0,8				0,36

148102..	RCACS 2,4 / 1,2			2,4         1,2				0,44

148103..	RCACS 3,2 / 1,6			3,2	  1,6				0,44

148104..	RCACS 4,8 / 2,4			4,8	  2,4				0,51

148106..	RCACS 6,4 / 3,2			6,4	  3,2				0,56

148109..	RCACS 9,5 / 4,8			9,5	  4,5				0,56

148112..	RCACS 12,7 / 6,4			12,7	  6,4				0,65

148119..	RCACS 19 / 9,5			19,0	  9,0				0,80

148125..	RCACS 25,4 / 12,7			25,4	  12,7				0,90

148138..	RCACS 38 / 19			38,0	  19,0				1,02

148151..	RCACS 51 / 25,5			51,0 	  25,5				1,14

148276..	RCACS  76 / 38  /on demand/	76,0	  38,0				1,14

148200..	RCACS  102 / 51  /on demand/	102,0	  51,0				1,30

148226..	RCACS  126 / 63,5  /on demand/	126,0	  63,5				1,30

148250..	RCACS  152 / 76   /on demand/	150,0	  76,0				1,30

The method of ordering:

Example   :                       50 pcs       RCACS  19/9,5      black

number of metres ________|                        |                      |____________ colour

type _______________________________|

-----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic            Telefax  +420 - 377 246 372

-----------------------------------------------------------------------------------------------------------------------------------

###### 1.1.2 Thin wall heat

shrinkable

tubes with sealant-

- RCK type

- flexible

- with the inside wall sealant

- good resistance against solvents and chemicals

- easy to cut

- colours: black, red, green, blue, yellow and transparent

- lengths: basic 1m, after an agreement even others, for example 50m on a spool

- shrink temperature more than 120ºC by hot air or soft yellow flame

- general use: in automotive industry, telecommunications, electronics  as an electric insulation from –55ºC up to +105ºC

- provides hermetically protected joints, mechanical protection

Packing: in closed folio with type indication

Storage:  in a sheltered place, temperature from –10ºC  up to +35ºC

##### Dimensions and types

Inside diameter 	    Wall thickness       Sealant thickness

Nr.                    Type	                   before and after	     after complete         after complete

d1 [mm] d2                 shrinking t mm        shrinking [mm]

142531..	RCK   3 / 1 		3,0	1,0		1,00			0,4

142541..	RCK   4 / 1 		4,0	1,0		1,00			0,4

142562..	RCK   6 / 2		6,0	2,0		1,20			0,5

142582..	RCK   8 / 2		8,0	2,0		1,20			0,5

The method of ordering:

Example   :                       50 pcs.         RC  4 / 1    – 1000       green

number of pieces ________|                        |                |              |____________ colour

type _______________________________|                |____________________ length

50 m             RC  4 / 1       green    on a spool

number of pieces ________|                        |                |___________________ colour

type _______________________________|

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.2 Thin wall

shrinkable

tubes

in a PE bag

- flexible

- mechanically durable

- excellent insulation

- suitable for marking the conductors

- without the inside sealant

Use:

- to mark cables and conductors or a bunch of conductors

- conductor endings

- suitable for  both hobby and work

Shrinking:

- shrinking temperature more than 120ºC by hot air or soft yellow flame

##### Types

Inside diameter           Wall

Nr.                      Type                 before and after     thickness       Length    Number         Colour

shrinking	    after shrinking    mm      of pieces

d1   mm  d2     	         t mm

14800200      RC 2,4/1,2             2,4       1,2                 0,51               30            40         black, green

14800300      RC 3,2/1,6             3,2       1,6                 0,51               30            36         black, green,

red, light blue

14800400      RC 4,8/2,4             4,8       2,4                 0,51               30            32         black, green

red, light blue

14800600      RC 6,4/3,2             6,4       3,2                 0,64	         30            30         black, green

red, light blue

14800800      RC 8/2	           8,0       2,0                 0,64               30            24         black, green

red, light blue

14800900      RC 9,5/4,8             9,5        4,8                0,64               30            26         black, green

red, light blue

14801200      RC 12,7/6,4          12,7       6,4                0,64               30            20         black, green

red, light blue

The method of ordering :		2 pcs.  RC  4,8/2,4  - 1 packing

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.3 Thin wall

heat shrinkable

tubes with

sealant,

type RCADW

Applications

Manufactured by co-extrusion of polyolefin and hot-melt adhesive. Designed to provide both insulation and sealing for protected articles. Used to protect auto wires, shipping cable, bundle

wires and metal tubes against water and moisture.

- basic length 1,22m , black colour

Features

Good electrical insulation and waterproof connection.

Packing: in closed folio with type indication

Storing:  in a sheltered place, temperature from –10ºC  up to +35ºC

##### Types and dimensions

Inside diameter before	  Wall thickness

Nr.                           Type			    and after shrinking               after shrinking

d1   mm  d2             		t mm

14227310	RCADW    3/1				 3 	 1			1,00

14227410	RCADW    4,8/1,5          		4,8       1,5			1,00

14227620	RCADW    6/2				 6       	 2			1,00

14227930	RCADW    9/3				 9	 3			1,40

14227120	RCADW  12/4			            12	 4			1,60

14227190	RCADW  19/6			            19	 6			2,15

14227240	RCADW  24/8			            24	 8			2,40

14227300	RCADW  30/10  /on demand/	30	10			2,40

14227400	RCADW  40/13  /on demand/	40	13			2,40

14227500	RCADW  50/19  /on demand/	50	19			2,40

Ordering :

Example   :                          50 pcs.   RCADW  6/2  –  1220      black

Number of pieces _______|                   |                   |             |_________ colour

Type ___________________________|                   |________________ length

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.4 Medium wall

heat shrinkable

tubes type RP

- universal and flexible

- RP type without the inside wall sealant

- good resistance against solvents, chemicals

- lengths: basic length 1m, it’s possible to arrange other lengths

RP types from 12/4 up to 52/20  max. 25m

- Colour: black, it’s possible to arrange other colours – brown, green, red

- Shrinking:  temperature more than 120ºC by hot air or soft yellow  flame

- Use: universal in industry. power electrotechnology up to 1kV, as a mechanic and electric protection of all kinds of whole-plastic cables

##### Types and dimensions

Inside diameter		   Wall thickness

Nr.		Type				       before and after                 after complete

shrinking		       shrinking

d1  mm d2                                              t mm

147109..	RP    9/3				9           3			2,0

147112..	RP  12/4				12         4			2,0

147117..	RP  17/3				17	 3			2,0

147118..	RP  18/6  / final sale  /		18	 6			2,0

147119..	RP  19/6				19	 6			2,0

147118..	RP  22/6				22         6			2,0

147125..	RP  25/10				25         10			2,0

147130..	RP  30/8				30         8			2,0

147132..	RP  32/12  / final sale  /		32	 12			2,0

147132..	RP  35/12				35         12			2,0

147141..	RP  40/12				40         12			2,1

147140..	RP  40/16				40         16			2,2

147150..	RP  50/16				50         16			2,2

147152..	RP  52/20				52         20			2,2

147163..	RP  63/27  / final sale  /		63	 27			2,5

147164..	RP  63/19				63         19			2,5

147175..	RP  75/22				75         22			3,0

147180..	RP  80/35				80         35			2,5

147195..	RP  95/30				95         30			3,5

147100..	RP 103/45				103       45			2,5

147315..	RP 115/34				115       34			3,3

147103..	RP 132/58				132       58			2,5

147114..	RP 140/42				140       42			3,5

Ordering:

Example:                               100 pcs   RP  63/19  –  1200      black

Number of pieces  _________|                  |              |             |_________     color

Type  ____________________________|              |________________     length

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.5 Medium wall

heat shrinkable

tubes

type RPK

- universal and flexible

- RPK tape with thermoplastic inside wall sealant has high adhesiveness to metals, steel, aluminium and lead

- good resistance against solvents, chemicals

- lengths: basic length 1m, it’s possible to arrange other lengths

RPK types max. 1,2m

- Colour: black, it’s possible to arrange other colours – brown, green, red

- Shrinking:  temperature more than 120ºC by hot air or soft yellow  flame

- Use: universal in industry. power electrotechnology up to 1kV, as a mechanic and electric protection of all kinds of whole-plastic cables

##### Types and dimensions

Inside diameter		   Wall thickness

Nr.		Type				       before and after                 after complete

shrinking		       shrinking

d1  mm d2                                              t mm

147309..	RPK    9/3				9           3			2,0

147312..	RPK  12/4				12         4			2,0

147316..	RPK  16/4				16	 4			2,0

147317..	RPK  17/3				17         3			2,0

147319..	RPK  19/6				19	 6			2,0

147321..	RPK  22/6				22         6			2,0

147325..	RPK  25/10				25         10			2,0

147330..	RPK  30/8				30         8			2,0

147332..	RPK  32/12  / final sale /		32         12			2,0

147332..	RPK  35/12				35         12			2,0

147341..	RPK  40/12				40         12			2,1

147340..	RPK  40/16				40         16			2,2

147350..	RPK  55/16				55         16			2,2

147352..	RPK  52/20				52         20			2,2

147364..	RPK  63/19				63         19			2,5

147364..	RPK  63/27  / final sale /		63         27			2,5

147375..	RPK  75/22				75         22			3,0

147380..	RPK  80/35				80         35			2,5

147395..	RPK  95/30				95         30			3,5

147300..	RPK 103/45				103       45			2,5

147315..	RPK 115/34				115       34			3,3

147303..	RPK 132/58				132       58			2,5

147314..	RPK 140/42				140       42			3,5

Ordering:

Example:                               100 pcs   RPK 63/19  –  1200      black

Number of pieces  _________|                  |              |             |_________     color

Type  ____________________________|              |________________     length

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.6 Thick wall heat

shrinkable tubes

RG, RGK types

- black

- RG type without the inside wall sealant

- RGK type with thermoplastic inside wall sealant has high adhesiveness to metals, steel, aluminium and lead

- lengths: basic length 1m, max. length 1,2m

- high resistance against solvents, chemicals

Shrinking:   temperature more than 120ºC by hot air of soft yellow flame

Use:             universal, for all kinds of whole-plastic cables as a mechanic protection or an electric

insulation up to 1 kV

Packing:      in closed folio with type indication

Storing:       in a sheltered place, temperature from –10ºC  up to +35ºC

##### Types and dimensions

Inside diameter		     Wall thickness

Nr.		Type		       before and after		     after complete	           Basic

shrinking	     	         shrinking	           length

d1  mm d2                                                  t mm                           mm

143119..	RG   19/6                 	19	 6			2,4			1000

143145..	RG   45/12		45	12			4,1			1000

143150..	RG   50/18*		50	18			3,5			1000

143151..	RG   55/16		55	16			4,1			1000

143160..	RG   60/25*		60	25			3,5			1000

143185..	RG   85/25		85	25			4,1			1000

143180..	RG   95/29		95	29			4,0			1000

143100..	RG 105/32		105	32			4,0			1000

143102..	RG 128/55*		128	55			4,0			1000

143102..	RG 140/34		140	34			4,0			1000

143165..	RG 165/50		165	50			4,5			1000

143319..	RGK   19/6		19	 6			2,4			1000

143334.. 	RGK   33/8		33	 8			3,0			1000

143345..	RGK   45/12		45	12			4,1			1000

143351..	RGK   55/16		55	16			4,1			1000

143360..	RGK   60/25*		60	25			3,5			1000

143378..	RGK   75/22		75	22			4,1			1000

143380..	RGK   80/32*		80        32			4,0			1000

143380..	RGK   95/29		95        29			4,0			1000

143300..	RGK 100/42*		100      42			4,0			1000

143300..	RGK 105/32		105      32			4,0			1000

143305..	RGK 115/34		115	34			4,1			1000

143330..	RGK 130/36		130	36			4,3			1000

143302..	RGK 140/34		140      34			4,0			1000

143365..	RGK 160/55		160	55			4,5			1000

143375..	RGK 180/50		180	50			4,3			1000

* final sale

Ordering :                               20 pcs   RGK 60/25  –  1000

Number of pieces __________|                 |                |

type  _____________________________|                | __________________ length

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.7 Heat shrinkable

tubes

RD, RDK types

with high shrink ratio

- black

- RD type without the inside wall sealant

- RDK type, after an agreement, with thermoplastic sealing tape, which has high adhesiveness to metals, steel, aluminium and lead

- lengths: basic length 1m, max. length 1,2m

- high resistance against solvents, chemicals

- Shrinking: temperature more than 120ºC by hot air of soft yellow flame

- Use: universal, for all kinds of whole-plastic cables as a mechanic protection or an electric insulation up to 1 kV, as an anti-corrosion protection of metal materials

Packing: in closed folio with type indication

Storing:  in a sheltered place, temperature from –10ºC  up to +35ºC

##### Types and dimensions

Inside diameter		     Wall thickness

Nr.		Type		       before and after		     after complete	           Basic

shrinking	     	         shrinking	           length

d1  mm d2                                                  t mm                           mm

14762200	RD   220/90		225     90			2,2			1000

14763000	RD   300/125		300     125			2,5			1000

14765000	RD   500/200		500     200			3,0			1000

14768200	RD   820/250		800      315			3,5			1000

14762210	RDK  220/90		225     90			2,2			1000

14763010	RDK  300/125		300     125			2,5			1000

14765010	RDK  500/200		500     200			3,0			1000

14768210	RDK  820/250		800      315			3,5			1000

Ordering :

Example   :                               20 pcs   RD 220/90  –  1000

Number of pieces __________|                 |                |

type  _____________________________|                |

length  ____________________________________|

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radyňská 24 , 326 00 Plzeň , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.8 Yellow-green heat

shrinkable tubes

- RCz, RPz types without the inside wall sealant

- RPKz type with the inside wall thermoplastic sealant

Use: for neutral conductor insulation

Nr.		Type		        Inner diameter		    Wall thickness

before and after		     after complete

shrinking (mm)		        shrinking

d1  mm d2                                                t mm

## Thin wall RCz

14830307	RCz   3,2/1,6		3,2	1,6			0,51

14800407	RCz   4,8/2,4		4,8	2,4			0,51

14800607	RCz   6,4/3,2		6,4	3,2			0,64

14800807	RCz   8/2		8,0	2,0			0,64

14800907	RCz   9,5/4,8		9,5	4,8			0,64

14801207   	RCz  12,7/6,4		12,7	6,4			0,64

14801907	RCz  19/9,5		19,0	9,5			0,76

14802507	RCz  25,4/12,7	24,4	12,7			0,89

14803807	RCz  38/19		38	19			1,02

14835107	RCz  51/25,5		51	25,5			1,02

## Medium wall without the inside sealant RPz

14700907	RPz     9/3		9	3			2,0

14701207	RPz   12/4		12	4			2,0

14701807	RPz   18/6		18	6			2,0

14702507	RPz   25/10		25	10			2,0

14703207	RPz   32/12		32	12			2,0

14704007	RPz   40/16		40	16			2,0

## Medium wall sealant-lined RPKz

14700907	RPK       9/3		9	3			2,0

14751207	RPKz   12/4		12	4			2,0

14751807	RPKz   18/6		18	6			2,0

14752507	RPKz   25/10		25	10			2,0

14753207	RPKz   32/12		32	12			2,0

14754007	RPKz   40/16		40	16			2,0

Ordering:  We supply the RCz types on a spool or cut into 1m pieces

it’s impossible to supply the RPz and RPKz types on a spool.

Example:                                  20 pcs   RPKz 32/12  –  1000

Number of pieces __________|                 |                   |

type  _____________________________|                   |

length ______________________________________|

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.9 Heat

shrinkable

terminations

- for all kinds of whole-plastic cables

- suitable for both indoor and outdoor surroundings

- protection against the soaking moisture into the cable

- protection against dangerous contact during measuring,

assembly, etc.

- green or yellow-green tube for neutral conductor

Packing:

- in closed folio with type indication

##### Types and dimensions

Nr.		Type			Cable diameters		    Tube length

mm²			         L mm

Four-cored      / AYKY, CYKY /   (2x black, 1x brown, 1x yellow-green)

14600124	KZ4X  6-25		4x6  -  4x25				50

14600186	KZ4X  16-50		4x16  -  4x50				70

14602510	KZ4X  70-95		4x70  -  3x95+70			80

14603212	KZ4X  95-150		3x95+70  -  3x150+70		100

14604016	KZ4X 185-240	3x185+95  -  3x240+120		120

Three-cored   / AYKY , CYKY /     (2x black, 1x brown)

14630124	KZ3  6-25		3x6  -  3x25				50

14630186	KZ3  16-50		3x16  -  3x50				70

14632510	KZ3  70-95		3x70  -  3x95				80

14633212	KZ3  95-150		3x95  -  3x150  			100

14634016	KZ3 185-240		3x185  -  3x240			120

Single-cored  / AYKY, CYKY /       (1x black)

14610124	KZ1  6-25		1x6  -  1x25				50

14610186	KZ1  16-50		1x16  -  1x50				70

14612510	KZ1  70-95		1x70  -  1x95				80

14613212	KZ1  95-150		1x95  -  1x150				100

14614016	KZ1 185-240		1x185  -  1x240			120

Ordering :                             10 pcs     KZ4X  70 - 95

Number of pieces _______|                   |________________    type

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

1.10 Heat shrinkable tubes,

no tracking,  type EAT

- universal and flexible

- no tracking red, heat shrinkable tubes for medium voltage applications.

- used mainly for high level insulation on medium voltage power cable terminations, up to 36 kV

- self extinguishing, halogen free.

Types and dimensions:

inner diameter                      wall thickness

No.                      Type           before and after shrinking       after complete shrinking

d1  mm d2                                                     t mm

14753010	EAT  30/10		30	10		   	    2,4

14754916	EAT  49/16		49	16			    2,9

14757026	EAT  70/26		70	26			    3,1

Ordering :

10 m      EAT 49/16  –  1000

Number of pieces _____|                  |                 |__________ length

Type            ___________________|

1.11 Heat shrinkable rain shed

- Non tracking red heat shrinkable rain shed, including internal hot-melt adhesive.

- Self extinguishing, halogen free

Use :

- used to increased external creepage length of power cable terminations.

| No. | Type | D | d | H | C | T1 | T2 | Weight g |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | ±5% | a | b |  |  |  |  | min | min |  |
|  |  | a | b | min | max | a | b | a | b | a | b | a | b |  |
| 14114415 | EIT1 44/15 | 95 | 95 | 44 | 15 | - | 40 | - | 20 | 1,5 | 3 | 3 | 3 | 35 |

a – before shrinking

b – after shrinking

----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o.   Radyňská  24 ,  326 00   Plzeň                                   Telefax   +420 - 377 246 372

----------------------------------------------------------------------------------------------------------------------------------

2. Cable accessories

2.1 Cable terminations

2.1.1 Heat shrinkable

terminations up to 1kV

- for all kinds of wholeplast cable endings

- protection against moisture entering the cable

- protection against dangerous contact during measuring

or assembly, etc.

- the inside-wall sealant-lined boot guarantees sealing the

cable core, the inside wall sealant-lined tubes seal the

space between the cable lugs and core insulation

- KSCZ4X type with following tube colours:

2x black; 1x brown; 1x yellow-green

##### Packing

- in a closed folio with type indication

##### Dimensions and types

Nr. 			Type			      For cable 		               Tube length

cross-section mm²		        L  mm

## Four-cored

14540124		KSCZ4X   6-25	4x6  -  4x25				50

14540186		KSCZ4X  16-50	4x16  -  4x50				70

14542510		KSCZ4X  70-95	4x70  -  3x95+70			80

14543212		KSCZ4X  95-150	3x95+70  - 3x150+70		    3x100+1x80

14544016		KSCZ4X 185-240	3x185+95  -  3x240+120	    3x125+1x100

## Five-cored

14550124		KSCZ5X  10-16	5x10  -  5x16				50

14550186		KSCZ5X  25-50	5x25  -  5x50				70

Ordering :                                        10 pcs       KSCZ4X   70-95

Number of pieces       ___________|                      |________________   type

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

2.1.2 Indoor cable termination

for three-cored cables

with plastic insulation

without semi-conductive

screen for 6 kV

Indoor cable termination is used for three-cored cables with plastic insulation without semi-conductive screen for 6 kV with Cu tape or Cu wires screen (AYKCY, CYKCY). For the wires are used non-tracking self-extinguishing halogen free shrinkable tubes. Non-tracking self-extinguishing halogen free shrinkable boots covers space between the end of the cable and the wires. Earthing of copper tape screen or lead sheath is provide by NPU kit which includes roll springs and tined copper net tape (NPU kit doesn’t supplied with the termination, it’s possible to order this kit separately).

Shrinking 	: by hot air with temperature over 120ºC or by soft yellow flame.

Storing     	: in a sheltered place between –10ºC and +35ºC

Nr.		         Type	        For cable cross-sections [mm²]	     Tube length L [mm]

14546301	KSCMTI 1    25 – 95		  25 – 95 			   500

14546302	KSCMTI 2    25 – 95		  25 – 95 			   1000

14546303	KSCMTI 1  120 – 240		120 – 240 		               500

14546304	KSCMTI 2  120 – 240		120 – 240 		               1000

- Termination kit includes tubes for three phases. Using of full cable lugs is recommended.

- It’s possible to order termination kit with different tube lengths or the tubes could be shorted before assembly. Min. tube length is 250mm.

Order:			KSCMTI 1  25-95      20 pcs

Termination type __________|        |              |___________ number of pieces

Cross-section _________________|

Kit for non-soldered connecting of earthing conductor for cables with copper tape screen or lead sheath

Nr.			Type		Cable cross-section [mm²]

13000025	      NPU   25 – 95		  25 – 95

13000120	      NPU 120 – 240		120 – 240

-----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-----------------------------------------------------------------------------------------------------------------------------------

2.1.3 Outdoor cable termination

for three-cored cables

with plastic insulation

without semi-conductive

screen for 6 kV

Outdoor cable termination is used for three-cored cables with plastic insulation without semi-conductive screen for 6 kV with Cu tape or Cu wires screen (AYKCY, CYKCY). For the wires are used non-tracking self-extinguishing halogen free shrinkable tubes. Non-tracking self-extinguishing halogen free shrinkable boots covers space between the end of the cable and the wires. Earthing of copper tape screen or lead sheath is provide by NPU kit which includes roll springs and tined copper net tape (NPU kit doesn’t supplied with the termination, it’s possible to order this kit separately). On each wire is slide up heat shrinkable rain shed.

Shrinking 	: by hot air with temperature over 120ºC or by soft yellow flame.

Storing     	: in a sheltered place between –10ºC and +35ºC

Nr.		         Type	                    For cable                    Tube length                Number

cross-sections [mm²]	 L [mm]                    of sheds

14546311	KSCMTO 1    25 – 95	            25 – 95		   500			3 x 1

14546312	KSCMTO 2    25 – 95	            25 – 95		   1000	 		3 x 1

14546313	KSCMTO 1  120 – 240         120 – 240 	               500			3 x 1

14546314	KSCMTO 2  120 – 240         120 – 240 		   1000			3 x 1

- Termination kit includes tubes for three phases. Full cable lug must be used !

- It’s possible to order termination kit with different tube lengths or the tubes could be shorted before assembly. Min. tube length is 450mm.

Order:			KSCMTO 1  25-95      20 pcs

Termination type __________|        |              |___________ number of pieces

Cross-section _________________|

Kit for non-soldered connecting of earthing conductor for cables with copper tape screen or lead sheath

Nr.			Type		Cable cross-section [mm²]

13000025	      NPU   25 – 95		  25 – 95

13000120	      NPU 120 – 240		120 – 240

-----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-----------------------------------------------------------------------------------------------------------------------------------

2.1.4 Indoor cable termination for

single-cored cables with plastic

insulation without

semi-conductive screen for 6 kV

Indoor cable termination is used for single-cored cables with plastic insulation without semi-conductive screen for 6 kV with Cu tape or Cu wires screen (AYKCY, CYKCY). For the wire is used non-tracking self-extinguishing halogen free shrinkable tube. Earthing of copper tape screen or lead sheath is provide by NPU kit which includes roll spring and tined copper net tape (NPU kit doesn’t supplied with the termination, it’s possible to order this kit separately).

Shrinking 	: by hot air with temperature over 120ºC or by soft yellow flame.

Storing     	: in a sheltered place between –10ºC and +35ºC

Nr.		         Type	                   	 	For cable                           Tube length

cross-sections [mm²]	           L [mm]

14546101	KSCMJI   120 – 500	         		120 – 500		              333

- Using of full cable lug is recommended.

- It’s possible to order termination kit with different tube length or the tube could be shorted before assembly. Min. tube length is 250mm.

2.1.5 Outdoor cable termination for

single-cored cables with plastic

insulation without

semi-conductive screen for 6 kV

Outdoor cable termination is used for single-cored cables with plastic insulation without semi-conductive screen for 6 kV with Cu tape or Cu wires screen (AYKCY, CYKCY). For the wire is used non-tracking self-extinguishing halogen free shrinkable tube and heat shrinkable rain shed. Earthing of copper tape screen or lead sheath is provide by NPU kit which includes roll spring and tined copper net tape (NPU kit doesn’t supplied with the termination, it’s possible to order this kit separately).

Shrinking 	: by hot air with temperature over 120ºC or by soft yellow flame.

Storing     	: in a sheltered place between –10ºC and +35ºC

Nr.		         Type	                   	 	For cable                           Tube length

cross-sections [mm²]	           L [mm]

14546111	KSCMJO   120 – 500	         		120 – 500		              333

- Full cable lug must be used !

- It’s possible to order termination kit with different tube length or the tube could be shorted before assembly. Min. tube length is 250mm.

Order:			KSCMJI   120-500      20 pcs

Termination type _______|              |                |___________ number of pieces

Cross-section _________________|

-----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-----------------------------------------------------------------------------------------------------------------------------------

2.2 Cable joints

2.2.1 Heat shrinkable

cable joints for

cables with plastic

insulation up to 1kV

The joint consists of the number of shrinkable tubes according to the number of cable cores. The cores can be combined by welding, or with the screwing or crimping joints. (crimping joints are not supplied.) The tubes substitute for the core insulation. The outer covering tube substitutes for cable sheathing. The tubes have the thermoplastic inside wall sealant of high adhesiveness. Shrink temperature is more than 120ºC by hot air or soft yellow flame.

Use         : for the AYKY, CYKY , NYY cable types, for rubber cables ( 2 outer covering tubes )

Packing  : in a closed folio with type indication and installation instructions

Storing   : in a sheltered place between –10ºC and +35ºC

Cable joint for four-cored cables with plastic insulation up to 1kV

Nr.           	Type		    Cable cross-section        Tube lengths

mm			L1 mm L2           Crimping joints

10122222	SVCZC    4-10         	   4 – 10 		330	80            4-10 Al, Cu

10122221	SVCZC    6-35	   6 – 35		450	125          6-35 Al, 6-50 Cu

10122224	SVCZC  16-50	  16 – 50		600	180	    16-50 Al, 16-70 Cu

10122225	SVCZC  35-150	  35 – 150		750	200	     35-150 Al, Cu

10122227	SVCZC  95-240	  95 – 240		850	240____   95-240 Al, Cu           _

Cable joints with screwing joints for cables with plastic insulation up to 1kV

Nr.		        Type		         For cable                                                        Number of

cross-sections [mm²]           Screwing joints         screw. joints

10127100	SVCZ  3x 1,5 – 6 S		1,5 – 6			1,5 – 6			       3

10127101	SVCZ  4x 1,5 – 6 S		1,5 – 6			1,5 – 6			       4

10127102	SVCZ  5x 1,5 – 6 S		1,5 – 6			1,5 – 6			       5

10127110	SVCZ  3x  4 – 16 S		 4 – 16			4 – 16			       3

10127111	SVCZ  4x  4 – 16 S		 4 – 16			4 – 16			       4

10127112	SVCZ  5x  4 – 16 S		 4 – 16			4 – 16			       5

10122111	SVCZC   6-35S	  	 6 – 35   		6-35 sm , 50 rm 	       4

6-35 re , 25 se

10122112	SVCZC   35-95S  		35 – 95   		25-95 rm , 25-70 sm         4

25-50  re , 70 se

10122113	SVCZC   70-150S		70 – 150                    	35-150 sm                         4

35-150 se,re

10122115	SVCZC   150-240S		150 – 240		3x 150-240 rm                 3+1

1x 35-150 sm,se,re

10122114	SVCZC  4x150-240S		150-240		150-240rm		       4

Order:

Example            :		10 pcs        SVCZC  4x 6-35S

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

2.2.2 Heat shrinkable

cable joints 0,6 / 1kV

for cable types

AYKY and CYKY

The advantage of these joints is their completeness for each cable cross-section. The joint consists of four shrinkable tubes for cable cores. The tubes substitute for insulation of the cores. The outer covering tube is black and substitutes for cable sheathing. All the tubes have the thermoplastic inside wall sealant of high adhesiveness. Four pieces of electroconductive aluminium or copper crimping cable joints for appropriate cable cross-section are included in separate cover.

Use        : for the AYKY or CYKY type cables

Packing : in a closed folio with type indication with installation instructions

Storing  : in a sheltered place between –10ºC and +35ºC

Nr.           	Type		          Cable cross-section	          Tube length     Number of pieces

mm			L1 mm L2    of the crimping joints

Setting the four-cored cables AYKY

10122400	SVCZC   16-Al		16			450	125		4

10122401	SVCZC   25-Al		25			450	125		4

10122402	SVCZC   35-Al		35			600	180		4

10122403	SVCZC   50-Al		50			600	180		4

10122404	SVCZC   70-Al		70			750	200		4

10122405	SVCZC   95-Al		95			750	200		4

10122406	SVCZC 120-Al		120			750	200		3+1

10122407	SVCZC 150-Al		150			750	200		3+1

10122408	SVCZC 185-Al		185			850	240		3+1

10122409	SVCZC 240-Al		240			850	240		3+1

Setting the four-cored cables  CYKY

10123498	SVCZC     6-Cu		6			330	80		4

10123499	SVCZC   10-Cu		10			330	80		4

10123400	SVCZC   16-Cu		16			450	100		4

10123401	SVCZC   25-Cu		25			450	125		4

10123402	SVCZC   35-Cu		35			500	125		3+1

10123403	SVCZC   50-Cu		50			600	180		3+1

10123404	SVCZC   70-Cu		70			600	180		3+1

10123405	SVCZC   95-Cu		95			700	200		3+1

10123406	SVCZC 120-Cu		120			800	200		3+1

10123407	SVCZC 150-Cu		150			800	200		3+1

10123408	SVCZC 185-Cu		185			900	240		3+1

10123409	SVCZC 240-Cu		240			900	240		3+1

Ordering :                                  10 pcs  SVCZC  120-Al

Four-cored cable ______________|           |     |

Cable cross-section   ____________________|     |________________ Al – crimping joints

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

2.2.3 Cable joints

for five-core

cables up to 1kV

The joint includes five heat shrinkable tubes ensuring core insulation and outer jacket tube on cable jacket. All tubes include on inner side thermoplastic sealant with high adhesivity.

Conductor connection can be performed by welding or with an aid of crimping joints.

Shrinking    : by hot air with the temperature more than 120ºC or by soft yellow flame

Application : for five-core plastic cables

Packing       : in a closed folio with type indication

Storing        : in sheltered place, temperature from –10ºC up to +35ºC

Nr.			Type			   Cable cross-section

(mm²)

Cable joints for five-core plastic cables

10124223		SVCZP   10 – 25		10 – 25

10124224		SVCZP   25 – 35		25 – 35

Cable joints for five-core plastic cables (inclusive of crimping joints) with copper cores

10125398		SVCZP     6 – Cu		      6

10125399		SVCZP   10 – Cu		    10

10125400		SVCZP   16 – Cu		    16

10125401		SVCZP   25 – Cu		    25

10125402		SVCZP   35 – Cu		    35

10125403		SVCZP   50 – Cu		    50

10125404		SVCZP   70 – Cu		    70

Cable joints for five-core plastic cables (inclusive of crimping joints) with aluminium cores

10124400		SVCZP   16 – Al		    16

10124401		SVCZP   25 – Al		    25

10124402		SVCZP   35 – Al		    35

Ordering :                                 10 pcs  SVCZP  16-Al

Five-core cable _______________|         |     |

Cable cross-section   ___________________|     |________________ Al – crimping joints

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

2.2.4 Joints for multi-cored cables with insulated

crimping joints

Crimping joints with shrinking

Outer sheath shrinkable tube				heat fusible inside wall

with heat fusible inside wall				sealant lined

sealant

L

Use                 : for multi-core cables with plastic insulation without armouring up to 1kV

Composition : the complete joint is  composed by  insulated  pressing  joints  which  number  is  in

accordance to  the  number  of  cable  cores  and  one  outer  sheath tube. Both the

sheath tube and the core shrinking tube ends are lined by a heat fusible  inside wall

sealant.

Packing : in a closed folio with type indication and installation instructions

Storing  : in a sheltered place between –10ºC and +35ºC

Nr.		Type / booking Nr. /            L /mm/             Cable diameter /mm/

min.                max.

10122503	SVCZV      3x0,5 – 1		330		7		17

10122504	SVCZV      4x0,5 – 1		330		7		17

10122505	SVCZV      5x0,5 – 1		330		9		24

10122507	SVCZV      7x0,5 – 1		330		9		24

10122512	SVCZV     12x0,5 – 1		330		11		31

10122519	SVCZV     19x0,5 – 1		330		11		31

10122524	SVCZV     24x0,5 – 1		380		15		39

10122537	SVCZV     37x0,5 – 1		380		15		39

10123503	SVCZV      3x1,5 – 2,5	330		9		24

10123504	SVCZV      4x1,5 – 2,5	330		9		24

10123505	SVCZV      5x1,5 – 2,5	330		9		24

10123507	SVCZV      7x1,5 – 2,5	330		9		24

10123512	SVCZV     12x1,5 – 2,5	330		11		31

10123519	SVCZV     19x1,5 – 2,5	380		15		39

10123524	SVCZV     24x1,5 – 2,5	380		15		39

10123537	SVCZV     37x1,5 – 2,5	380		15		39

10123548	SVCZV     48x1,5 – 2,5	380		15		39

10124503	SVCZV      3x4 – 6		330		9		24

10124504	SVCZV      4x4 – 6		330		9		24

10124505	SVCZV      5x4 – 6		330		11		31

10124507	SVCZV      7x4 – 6		330		11		31

10124512	SVCZV     12x4 – 6		330		15		39

Ordering  :                             10 pcs   SVCZV    7 x 1,5

Multi-core cable _____________|           |       |_________ core cross-section

|_____________ number of cores

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

2.2.5 Joints for three-core

plastic cables without

semi-conductive

screen up to 6kV

- joints for cables with copper wire or copper tape screen (AYKCY,CYKCY)

- the core connection is covered by a tape and heat shrinkable tube with sealant ensures insulation and water sealing of the cores. Screen wires are connect by net tape with an aid of roll spring. On outer jacket is shrunk thick wall shrinkable tube with sealant.

Nr.                                  Type                              U(/U (kV) _

10126301         	SVCMT   25-50	          	3,5/6

10126302	       	SVCMT   70-150	          	3,5/6

10126303	       	SVCMT 185-240	        	3,5/6

10126311	      	SVCMT   25-Al		3,5/6

10126312	       	SVCMT   35-Al		3,5/6

10126313	       	SVCMT   50-Al		3,5/6

10126314            	SVCMT   70-Al		3,5/6

10126315		SVCMT   95-Al		3,5/6

10126316		SVCMT 120-Al		3,5/6

10126317		SVCMT 150-Al		3,5/6

10126318                   SVCMT 185-Al	3,5/6

10126319		SVCMT 240-Al		3,5/6

2.2.6 Joints for single-core plastic cables without

semi-conductive screen up to 6kV

- joints for cables with copper wire or copper tape screen (AYKCY,CYKCY)

- the core connection is covered by a tape and heat shrinkable tube with sealant ensures insulation and water sealing of the core. Screen wires are connect by net tape with an aid of roll spring. On outer jacket is shrunk thick wall shrinkable tube with sealant.

Nr.                                  Type                               U0/U (kV)_

10126101         	SVCMJ   300-500	        3,5/6

Ordering :                     10pcs  SVCMT 25-50            10ks   SVCMTP 25-Al

Type ____________________|______|_________________|            |

Cable cross-section _________________|________________________|

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

3. Accessories

3.1 Heat shrinkable

cable end

caps

for all kinds

of whole-plastic

cable ending

- with thermoplastic inside wall sealant

- they enable closing the cable end secure it against

moisture entering the cable

- shrink temperature more than 120ºC by hot air or

soft yellow flame

Use          : for storing the cable or it’s transport. Alive

cables up to 1kV ; -55ºC to +105ºC

Dielectric strength :  16 kV/mm

Color       : black

Storing    : in a sheltered place, temperature from –30ºC

up to +35ºC

Packing  : in closed folio with type indication

##### Basic parameters

Inside diameter	         Wall    	         							         Length		  Cable

Nr.		Type		     before and after	      thickness	         before		diameters

after shrinking	  after shrinking      shrinking	                mm

mm		          mm		mm		from up to

14102001	KTk  10/4		10	4		2,4		48		5	9

14102009	KTk  21/6		21	6		2,1		15		7	19

14102002	KTk  23/8		23	8		2,9		85		9	20

14102003	KTk  33/15		33	15		3,5		106	           16	30

14102006	KTk  40/15		38	15		3,5		106                 16	36 14102004	KTk  52/25		52	25		3,5		160	           27	50 14102007	KTk  70/25		70	25		3,5		125	           27         66 14102005	KTk  90/45		90	45		4,7		160	           47         88

Ordering:

Example:                          100 pcs           KTk   33 / 15

Type                                            _____|        |      |

Inside diam. before shrinking       _________|      |

Inside diam. after shrinking         _____________|

-----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-----------------------------------------------------------------------------------------------------------------------------------

3.2 Heat-shrinkable breakouts

- used to protect cable terminations against moisture

- special inside wall sealant guarantees tightness

- easy shrinking assembly with soft yellow flame or more than 135ºC hot air

- suitable for both indoor and outdoor applications

- the shrinking parts should be at least 5mm larger than the cable diameter

- the cable should be cleaned and pre-heated before sealing

- start shrinking in the middle of the breakout and continue up and down to the ends

Types and technical data:

Nr.	           Type		D1	D1*	D2	D2*	L1	L2	W1*	W2*      cable

diameter

14213015	EN 2		30	10	14	4,0	90	25	2,0	2,0	6-25

14315630	EN 3.1		52	22	22	8,0	180	45	3,0	2,0	70-150

14328045	EN 3.2 	78	35	36	16,0	210	50	4,0	3,0	185-300

14413516	EN 4.1		38	15	13	4,0	90	20	2,5	2,0	6-50

14435525	EN 4.3		60	26	25	8,0	170	30	3,3	2,5	50-150

14457838	EN 4.5		90	44	33	13	210	40	4,0	3,5	185-300

14514311	EN 5.1		43	18	11	3,8	175	60	2,8	2,8	10-35

14526030	EN 5.2		60	25	30	7,5	180	30	3,5	3,0	35-95

* recovered

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

3.3 TPM – brickwork bushing

Use:

TPM – brickwork bushing is used for sealing a cable passing through a brickwork.

Characteristics:

- waterproofed

- gasproofed

- resistant against chemicals

- resistant against climatic changes

L: Length before shrinking

Nr.		Type		         Cable diameter	         Bushing		    Max. brickwall

in  mm	          length	                  width in mm

min.	max.	         L (mm)

14701410	TPM – 14/10		10   -	14		800			500

14702312	TPM – 23/12		12   -	23		800			500

14702816	TPM – 28/16		16   -	28		800			500

14703820   	TPM – 38/20		20   -	38		800			500

14705027	TPM – 48/27		27   -	48		800			500

14708645	TPM – 86/45		45   -	86		800			500

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

3.4 Heat shrinkable repairing sleeves for cables

with plastic or paper insulation

Application:

Heat-shrinkable repairing sleeve SM is used for quick, high quality and heavy-duty repairs of damaged cable sheaths. It guarantees sealing against water entering cable insulation. It substitutes for plastic cable sheath and plastic anticorrosive metal sheath protection. The metal connecting strip can be removed after complete cooling down the sleeve.

Č.                			Typ

14642825		SM 42/8 - 250

14642850		SM 42/8 - 500

14642875		SM 42/8 - 750

14642800		SM 42/8 - 1000

14650125		SM  50/10 - 250

14650150		SM  50/10 - 500

14650175		SM  50/10 - 750

14650100		SM  50/10 - 1000

14675050		SM  75/22 – 500                           Dimensions:

14675100		SM  75/22 – 1000			D:  inner diameter

L :  length before shrinking

14690050		SM  93/36 – 500

14690100		SM  93/36 – 1000

14610050		SM 100/30 – 500

14610100		SM 100/30 – 1000

14612050		SM  135/38 – 500

14612100		SM  135/38 – 1000

Ordering :                     	       SM    42/8  -  250     2pcs

Inside diameter before shrinking ______|    |         |          |_______ Number of pieces

Inside diameter after shrinking  _________|         |_____________ Sleeve length before shrinking

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

Electro-insulating repairing

tape with adhesive - TKT

They are recommended where the execution of durable and leakproof connection of structural components is required. Good adhesion to metallic, wooden components and to building ceramics and plastics gives the possibility to apply the heat shrinkable tapes by the mounting of ventilation pipes, conductors, electric and telecommunication cables. Connections made of TKT tape are resistant to mechanical damages and corrosion.

No.		         Type		          Length  	    Width     Thickness

m	     mm	 	mm

14810250	TKT  –  25 / 05 / 03		30	      25	 	0,5

14810500	TKT  –  50 / 05 / 03		30	      50	 	0,5

14811000	TKT – 100 / 05 / 03		30	     100	 	0,5

14811500	TKT – 150 / 05 / 03		30	     150	 	0,5

14810501	TKT  –  50 / 1 / 03		30	      50	 	1,0

Ordering :

Example    :                                10 pcs              TKT – 25/05/03

Number of pieces       _________|                             |

Type              ______________________________|

----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o.   Radynska  24 ,  326 00   Plzen                                 Telefax    00420 377 246 372

----------------------------------------------------------------------------------------------------------------------------------

3.6 Heat shrinkable insulated crimping joints

Connection element is composed by a compression joint and heat shrinkable sealant-lined tube put on it.

Use:

For connecting conductors in electroinstallations

up to 1kV. Shrinking temperature 110ºC-200ºC.

Nr.			 Type 	       Conductor cross-section ( mm²)			Colour

14033041		DR  1			0,5  -  1,0				red

14033042		DR  2			1,5  -  2,5				blue

14033043		DR  3			4,0  -  6,0				yellow

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

3.8 Shrinkable tube set

ZDM – 1 , ZDM – 2

Use:

- in household – to wend electrical appliances such as refrigerators, vacuum cleaners, iron, electronically appliances, etc.

- in technology of modellers, fishermen

- as an insulation of hand tools – pliers, screwdrivers, etc.

Specification:  ZDM – 1 type               Nr. 14800001

Nr.  Contains     Type			 L       Number of pcs.

1   Shrinkable	RC   2,4/1,2		95		60

2      tubes	RC   3,2/1,6		95		40

3		RC   4,8/2,4		95		24

4		RC   6,4/3,2		95		14

5		RC  12,7/6,4		95		 2

6		RC  19,0/9,5		95		 2

7		RC  25,4/12,7		95		 2

8 		RC   2,4/1,2		195		 3

9   		RC   3,2/1,6		195		 2

10		RC   4,8/2,4		195		 3

11		RC   6,4/3,2		195		 2

12		RC   9,5/4,8		195		 1

13		RC  12,7/6,4		195		 1

Specification :  Type ZDM – 2               Nr. 14800002

Nr.   Contains    Type			 L       Number of pcs.

1		RC   1,6/0,8		55		60

2   Shrinkable	RC   2,4/1,2		55		30

3      tubes	RC   3,2/1,6		55		25

4		RC   4,8/2,4		55		15

5		RC   6,4/3,2		100		15

6		RC   9,5/4,8		100		 8

7		RC  12,7/6,4		100		 8

8		RC  19,0/9,5		100		 3

9 		RC   12,0/4,0		100		 6

- Cable

terminal   B  311					10

11   Soft solder			350		 3

12   Clamp	             				10

Case size               :	210 x 105 x 50 mm

Weight                    :	ZDM-1  0,27 kg,   ZDM-2   0,31 kg

Dielectric strength  :	up to 1 kV

Shrinking                :	temperature more than 120ºC by hot air or soft yellow flame

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

3.10 Cu/Al washer

Application:

Al-Cu washers eliminate a minicells creating effect on the contact of two different metals. The washers applied to efectricai circuits cause reduction of energy loss. They increase the safety and the life of connection.

Except the application in power engineering, the washers can be used in electrical installations for the connection of parts made of aluminum and copper.

Technical data:

Cable washers are made of aluminum bars in the recrystallizing condition of AOE and A1E grade (PN 92/H-93667.01) and copper bars in the recrystallizing condition of M1E grade (PN

82/H-93620.0).

Nr.			  Type	        D  (mm)	         d  (mm)         G (mm)

10000008		PC  3,5	8,5		3,5		1

10000005		PC  5,5	11		5,5		1

10000006		PC  6,5	13		6,5		1

10000001		PC  8,5	19		8,5		1

10000002		PC  11		24		11		1

10000003		PC  13		30		13		1

10000004		PC  17		38		17		1

10000007		PC  19/6,5	19		6,5		1

10000009		PC   21	38		21		1

3.11 Insulating clamp

UP – 22, UP – 30, UP – 50 types for insulated conductors

Description:

The insulating clamp is made from white or black polyethylene with elastic tape that helps to fix the conductor quickly.

Use:

The clamp is used for insulated conductor assembly. The conductor diameter should be between 7,5 and 22 mm. The clamp is fixed on the subsurface by a screw.

Nr.			Type			L		T		P

14000001		UP  -  22		96		17		28

14000002		UP  -  30 		140		23		37

14000003		UP  -  50		220		52		61

-----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-----------------------------------------------------------------------------------------------------------------------------------

3.12 The UKU – 50 type

universal cable clamp

Use:

The cable clamp is used for fixing cables with diameter from 28 to 50 mm.

Nr.  14000004

3.13 Roll

springs

- for connection copper screen or lead or aluminium cable jacket

- simple installation without tools – wrapping the roll spring

- provides current passage through hole circuit

Nr.                      Type         Min. diameter        Max. diameter

# mm        	          mm

# 14050001            S1                    18                          29

# 14050002            S2                    23			 27

# 14050003	     S3                    26			 44

# 14050004	     S4		      31			 50

# 14050005 	     S5		      38			 68

# 14050006	     S6		      58			 94

-----------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-----------------------------------------------------------------------------------------------------------------------------------

### 3.15 Compression joints Al and Cu

For circular stranded aluminium or copper, circular stranded, sector shaped stranded, circular solid and sector shaped solid aluminium or copper conductors.

For non-tension connections.

Conductor              ø mm            Dimensions mm       Packing          Weight

Nr.	    cross-section         conductor         d          l          D          unit                  kg

# Compression joints Al

10628055	16		4,4 - 5,4	5,5	65	9,5	   10		0,007

10628065	25		5,4 - 6,4	6,5	70	11,5	   12		0,010

10628080	35		6,6 - 7,8	8,0	75	14,0	   14		0,020

10628095	50		7,6 – 8,9	9,5	85	15,5	   16		0,023

10628110	70		9,3 – 10,7	11,0	105	18,0	   18		0,033

10628130	95		11,0 – 12,6	13,0	105	21,0	   21		0,060

10628145	120		12,5 – 14,2	14,5	115	24,5	   24/25	0,092

10628160	150		13,7 – 15,7	16,0	125	25,0	   24/25	0,095

10628180	185		15,3 – 17,6	18,0	133	28,0	   28		0,144

10628210	240		17,5 – 20,2 	21,0	140	32,0	   32		0,191

# Compression joints Cu

10627006	 6		5

10627010	10		4,1		4,5	32	6,0	   6

10627016	16		5,1		5,7	50	8,5	   8

10627025	25		5,6-6,5		7,0	50	10,0	  10

10627035	35		6,6-7,5		8,2	50	12,5	  12

10627050	50		7,7-8,6		10,0	55	14,5	  14

10627070	70		9,3-10,2	11,5	55	16,5	  16

10627095	95		11,0-12,0	13,5	70	19,0	  18

10627120	120		12,5-13,5	15,5	70	21,0	  20

10627150	150		13,9-15,0	17,0	80	23,5	  22

10627185	185		15,5-16,8	19,0	85	25,5	  25

10627240	240		17,8-19,2	21,5	90	29,0	  28

Sector-shaped conductors must be rounded with rounding jaws.

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

3.16 The PBSH 3 soldering set

Nr. 30150001

Use:

- Soldering set PBSH 3 is meant for soft soldering, for hard soldering thin sheets with solder with working  temperature  up  to  800ºC,  for  shrinking, removing old coats of paint, and for various kinds  of  hearing.  Propane-butane  (basic composition 60% P + 40 % B )  and  primary  air are used.

- It consists of a handle with quick-operating valve and regulatable gas saver, a Lomat Piezo30 burner, PB-closing valve, connecting tubing 2,5 m and multi-opening wrench. The whole set is in metal case.

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

4. Cable assembly tools

4.1 Cable knifes, pliers

The shuttled knife NSC 1

This shuttled knife is used to remove the cable insulation off.

Nr. 11100001

Straight cable knife

Nr. 11000002

The knife for rubber NG

Nr. 11000005

The knife NZ

Nr. 11000004

The pressing pliers K 2

These pressing pliers are used to press on insulated joints. For diameters between 0,5 – 6 mm.

Nr. 30140002

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

# 4.2 Hydraulic and electric tools

# Foot-operated hydraulic pump           Nr.  30240001

HYG-N-80T

Purpose:        source of pressure for hydraulic tools

Description:   Hydraulic  generator  is  a  compact  unit   with   the  piston

pump, pressure	 relief valve, oil reservoir and lever arm for

foot operation.  Generator  is  equipped  with high pressure

hose for quick coupling. The lever arm of unit is shaped as

a handle to be carried easily.

Technical        dimensions – length…620 mm         height…200mm

specification:                       width…200 mm           weight…7kg

oil tank……………….1,2 l

hose’s length………..2 m

operating pressure…80 MPa

Hydraulic crimping head		Nr.   30230001

LH 6,5

Purpose:       For  all  types  of  crimping  jobs  on  aluminium  cables  till

240 mm² of cable grips and terminals especially in cramped

room.

Description:  Hydraulic  crimping  head  LH 6,5  is  constructed both for

co-operation     with        foot-operated     hydraulic    pump

HYG-N-80T   and    motor-operated       hydraulic       pump

HYG-E-802. All these devices   are   equipped   with  quick

couplings  for  easy  connection.  LH 6,5  is  delivered  with

optional set of hexagonal crimping dies.

Technical       dimensions – length…280 mm      weight…2,6 kg

specifications:                        width…48 mm

height…78 mm

hexagonal crimping dies: 16,25,35,50,70,95,120+150,185,240 mm²

Rounding jaws			Nr. 4010090 – set in a case

Rounding and shaping jaws for LH 6,5 – pressing head

determined

Nr.	       Marking             ø d     for cross-section    Weight

mm             (mm²)                 kg_______

Rounding jaws

40009512        95/12,5          12,5                95	      0,49

40012013       120/13,5         13,5	              120	      0,49

40015015       150/15            15,0	              150	      0,47

40018517        185/17            17,0	  185	           0,44

40024019       240/19,2          19,2	  240                 0,41

Shaping jaws                                               Shaping jaws

40000090            -                     -	                -	      0,30______

Use:  Rounding jaws:

to round Al and Cu se/sm cable cores

Shaping jaws:

to bend strip to 90º, to shape conductors up  to  ø9 mm,  to  shape

earthing  strip  and  Al  and  Cu  strip  up  to  9 mm  thickness  and

40 mm width.

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

# 4.3 Other tools

# Hand-operated punching tool		Nr.  30110001

DZP – 11

Use:   for punching holes of diameter 11 mm  into the earthing strips

( e.g. 30 x 4 mm zinc-coated metal strip)

Technical   dimensions – length…455 mm       weight…2,1 kg

width…..42 mm

height…110 mm

Gradual cables-cutter			Nr.  30120002

# PN-AL-40

Use:  for gradual cutting of the aluminium cables and cable cores

till 40mm of diameter.

Technical    dimensions – length…635 mm        height…110 mm

width…..22 mm          weight…2,8 kg

# Distance-measuring wheels TK 100

Distance-measuring wheel TK-100 (wheel average 36 cm) allows numerical reading of longitude. Measuring range of TK-100 is 0 – 9.999 m. Longitude is possible read lengthways 1cm. Analogue counter with possibility of reset is set in lower parts of folding handle, above the wheel (counter on drive astern is countdown – possibility of corrections trace out course). Distance-measuring wheel is equipped with a wheel brake and a jack.

-------------------------------------------------------------------------------------------------------------------------------

SKELDO s.r.o. , Radynska 24 , 326 00 Plzen , Czech Republic       Telefax  +420 - 377 246 372

-------------------------------------------------------------------------------------------------------------------------------

# Text boxes

sealant

### SKELDOO®KELDO